## Slide 1: YANG models for ACTN TE Performance Monitoring Telemetry and Network Autonomics draft-lee-teas-actn-pm-telemetry-autonomics-07
Young Lee, Dhruv Dhody, Satish K, Ricard Vilalta, Daniel King, Daniele Ceccarelli

## Slide 2: Overview
YANG data models that support
  Performance Monitoring (PM) Telemetry for Tunnel and VN level:
    ietf-te-kpi-telemetry
    ietf-actn-te-kpi-telemetry
  Network autonomics for Scaling Intent (for TE-tunnels and ACTN VNs.)
  ACTN CMI Model – Customer-Driven Model
Use-case: [I-D.xu-actn-perf-dynamic-service-control-03]
  Performance Monitoring
  Dynamic control in ACTN – creation, modification, optimization etc.
  Monitor Network Traffic, Detects traffic imbalance, Initiate optimization!
  Measure customer SLA, take dynamic action to make sure you meet them at all times
  Scalability of Performance data

## Slide 3: Yang Model Relationships ietf-te-kpi-telemetry & ietf-actn-te-kpi-telemetry
TE Tunnel
TE KPI Telemetry
Augments
ACTN VN
ACTN TE Telemetry
Augments
TE KPI Telemetry model provides the TE tunnel level performance monitoring.
Augment the TE tunnel State with performance attributes
  Use the notification subscription (YANG PUSH)
Scaling Intent configurations for auto scaling in/out based on the combination of the performance monitored attributes
ACTN TE KPI Telemetry model provides the VN level aggregated performance monitoring.
Augment the VN state as well as individual VN-member state with performance attributes.
  Use notification subscription (YANG PUSH)
Scaling Intent configurations at the VN level to reach to the monitored performance KPI
Example:
(one-way-delay > 50ms) AND (one-way-packet-loss > 1%)
-> Triggers TE Scale In

## Slide 4: Status
Presented in IETF 100.
One major comment was: augment/re-use existing grouping(s) for performance data.
This version made that change:
  Basically imported TE-Types and uses the grouping defined in TE-types: performance-metric-attributes where uni-directional PM are defined for link and applied them to be used for connections (tunnels).
  Added bi-directional performance monitoring data for connections (tunnels) in the module ietf-te-kpi-telemetry defined in this draft to give a full list of PM data.

## Slide 5: Changes in the YANG module ietf-te-kpi-telemetry
augment "/te:te/te:tunnels/te:tunnel" {
container te-telemetry {
config false;
description
"telemetry params";
leaf id {
type string;
description "Id of telemetry param";
}
uses te-types:performance-metric-attributes;
/* all unidirectional PM data is defined in this grouping */
uses bidirectional-telemetry-data;
/* all bidirectional PM data is defined in this grouping */
leaf te-ref {
type leafref { path '/te:te/te:tunnels/te:tunnel/te:name';
}
description "Reference to measured te tunnel";
}
}
Re-uses a grouping defined in te-types
for uni-directional PM data
Define a grouping in this module
for bi-directional PM data

## Slide 6: Changes in the YANG module ietf-actn-te-kpi-telemetry
augment "/vn:actn/vn:vn/vn:vn-list/vn:vn-member-list" {
description
"Augmentation parameters for state TE vn member topologies.";
topologies.";
container vn-telemetry {
config false;
description
"VN member telemetry params";
uses te-types:performance-metric-attributes;
uses te-kpi:bidirectional-telemetry-data;
uses vn-telemetry-param;
}
}
Re-uses a grouping defined in te-types
for uni-directional PM data
Re-uses a grouping defined in te-kpi
for bi-directional PM data

## Slide 7
module: ietf-te-kpi-telemetry
augment /te:te/te:tunnels/te:tunnel:
+--rw te-scaling-intent
| +--rw scale-in-intent
| | +--rw threshold-time? uint32
| | +--rw cooldown-time? uint32
| | +--rw scale-in-operation-type? scaling-criteria-operation
| | +--rw scale-out-operation-type? scaling-criteria-operation
| | +--rw scaling-condition* [performance-type]
| | +--rw performance-type identityref
| | +--rw te-telemetry-tunnel-ref? -> /te:te/tunnels/tunnel/name
| +--rw scale-out-intent
| +--rw threshold-time? uint32
| +--rw cooldown-time? uint32
| +--rw scale-in-operation-type? scaling-criteria-operation
| +--rw scale-out-operation-type? scaling-criteria-operation
| +--rw scaling-condition* [performance-type]
| +--rw performance-type identityref
| +--rw te-telemetry-tunnel-ref? -> /te:te/tunnels/tunnel/name
+--ro te-telemetry
+--ro id? string
+--ro unidirectional-delay? uint32
+--ro unidirectional-min-delay? uint32
+--ro unidirectional-max-delay? uint32
+--ro unidirectional-delay-variation? uint32
+--ro unidirectional-packet-loss? decimal64
+--ro unidirectional-residual-bandwidth? rt-types:bandwidth-ieee-float32
+--ro unidirectional-available-bandwidth? rt-types:bandwidth-ieee-float32
+--ro unidirectional-utilized-bandwidth? rt-types:bandwidth-ieee-float32
+--ro bidirectional-delay? uint32
+--ro bidirectional-min-delay? uint32
+--ro bidirectional-max-delay? uint32
+--ro bidirectional-delay-variation? uint32
+--ro bidirectional-packet-loss? decimal64
+--ro bidirectional-residual-bandwidth? rt-types:bandwidth-ieee-float32
+--ro bidirectional-available-bandwidth? rt-types:bandwidth-ieee-float32
+--ro bidirectional-utilized-bandwidth? rt-types:bandwidth-ieee-float32
+--ro utilized-percentage? uint8
+--ro te-ref? -> /te:te/tunnels/tunnel/name
module: ietf-actn-te-kpi-telemetry
augment /vn:actn/vn:vn/vn:vn-list:
+--rw vn-scaling-intent
| +--rw scale-in-intent
| | +--rw threshold-time? uint32
| | +--rw cooldown-time? uint32
| | +--rw scale-in-operation-type? scaling-criteria-operation
| | +--rw scale-out-operation-type? scaling-criteria-operation
| | +--rw scaling-condition* [performance-type]
| | +--rw performance-type identityref
| | +--rw te-telemetry-tunnel-ref? -> /te:te/tunnels/tunnel/name
| +--rw scale-out-intent
| +--rw threshold-time? uint32
| +--rw cooldown-time? uint32
| +--rw scale-in-operation-type? scaling-criteria-operation
| +--rw scale-out-operation-type? scaling-criteria-operation
| +--rw scaling-condition* [performance-type]
| +--rw performance-type identityref
| +--rw te-telemetry-tunnel-ref? -> /te:te/tunnels/tunnel/name
+--ro vn-telemetry
+--ro unidirectional-delay? uint32
+--ro unidirectional-min-delay? uint32
+--ro unidirectional-max-delay? uint32
+--ro unidirectional-delay-variation? uint32
+--ro unidirectional-packet-loss? decimal64
+--ro unidirectional-residual-bandwidth? rt-types:bandwidth-ieee-float32
+--ro unidirectional-available-bandwidth? rt-types:bandwidth-ieee-float32
+--ro unidirectional-utilized-bandwidth? rt-types:bandwidth-ieee-float32
+--ro bidirectional-delay? uint32
+--ro bidirectional-min-delay? uint32
+--ro bidirectional-max-delay? uint32
+--ro bidirectional-delay-variation? uint32
+--ro bidirectional-packet-loss? decimal64
+--ro bidirectional-residual-bandwidth? rt-types:bandwidth-ieee-float32
+--ro bidirectional-available-bandwidth? rt-types:bandwidth-ieee-float32
+--ro bidirectional-utilized-bandwidth? rt-types:bandwidth-ieee-float32
+--ro utilized-percentage? uint8
+--ro grouping-operation? grouping-operation
augment /vn:actn/vn:vn/vn:vn-list/vn:vn-member-list:
+--ro vn-member-telemetry
+--ro unidirectional-delay? uint32
+--ro unidirectional-min-delay? uint32
+--ro unidirectional-max-delay? uint32
+--ro unidirectional-delay-variation? uint32
+--ro unidirectional-packet-loss? decimal64
+--ro unidirectional-residual-bandwidth? rt-types:bandwidth-ieee-float32
+--ro unidirectional-available-bandwidth? rt-types:bandwidth-ieee-float32
+--ro unidirectional-utilized-bandwidth? rt-types:bandwidth-ieee-float32
+--ro bidirectional-delay? uint32
+--ro bidirectional-min-delay? uint32
+--ro bidirectional-max-delay? uint32
+--ro bidirectional-delay-variation? uint32
+--ro bidirectional-packet-loss? decimal64
+--ro bidirectional-residual-bandwidth? rt-types:bandwidth-ieee-float32
+--ro bidirectional-available-bandwidth? rt-types:bandwidth-ieee-float32
+--ro bidirectional-utilized-bandwidth? rt-types:bandwidth-ieee-float32
+--ro utilized-percentage? uint8
+--ro te-grouped-params* -> /te:te/tunnels/tunnel/te-kpi:te-telemetry/id
+--ro grouping-operation? grouping-operation
ietf-actn-te-kpi-telemetry
ietf-te-kpi-telemetry

## Slide 8: Next Steps
This draft provides Customer-programmable PM telemetry and Network Automatics on the CMI of ACTN architecture.
The authors believe this draft has a good base for WG adoption 