## Slide 1: Traffic Engineering and Service Mapping Yang Model draft-lee-teas-te-service-mapping-yang-09
Young Lee, Huawei
Dhruv Dhody, Huawei
Daniele Ceccarelli, Ericsson
Jeff Tantsura, Nuage Networks
Giuseppe Fioccola, Telecom Italia
Qin Wu, Huawei
TEAS WG @ IETF 102

## Slide 2: TE-Service Mapping Model Update
The role of TE-service Mapping model is to create a mapping relationship between -
  Services – L3SM, L2SM, L1CSM, etc.
  TE topo, TE tunnel model and the ACTN VN Model
  Update: Generalized it by making the model to have direct mapping to TE-topo and TE-tunnel as well!
This TE-service mapping model is needed to bind L3VPN, L2VPN, L1CSM specific service model with underlying TE-specific parameters.
This binding will facilitate a seamless service operation with underlay-TE network visibility.
L3SM
L2SM
TE-Service Mapping Model
ACTN VN
TE-topology
L1CSM
TE-tunnel
Generalization

## Slide 3: Issues discussed since IETF 101
One TE & Service Mapping YANG module vs. Three separate augmented L1/2/3 SM models.
WG discussions were in favor of having one TE & Service Mapping model that applied to all L1/2/3 SM models.
CNC
MDSC
CNC
MDSC

## Slide 4: TE-Service Mapping Model Update (2)
Reorganized Map Type (for VN/Tunnel selection policy)
New VN/Tunnel Binding
Customer could request a VPN service with a new VN/Tunnel not shared with other existing services.
VN/Tunnel Sharing
Customer could request a VPN where the tunnels can be shared with other existing VPNs.
VN/Tunnel Modify
This mode allows the modification of the properties of the existing VN/tunnel (e.g., bandwidth) when VN/Tunnel Selection Mode is applied.
Hard Isolation with deterministic characteristics
Hard Isolation
Soft Isolation

## Slide 5: TE-Service Mapping Model Update (3)
Introduced “Availability” for customer to indicate the level of availability.
  99.9999
  99.999
  99.99
  99.9
  99
This needs to be translated into network level protection/reroute level.

## Slide 6: Yang Model
module: ietf-te-service-mapping
+--rw te-service-mapping
+--rw service-mapping
| +--rw mapping-list* [map-id]
| +--rw map-id uint32
| +--rw map-type? map-type
| +--rw (service)?
| | +--:(l3vpn)
| | | +--rw l3vpn-ref? -> /l3:l3vpn-svc/vpn-services/vpn-service/vpn-id
| | +--:(l2vpn)
| | | +--rw l2vpn-ref? -> /l2:l2vpn-svc/vpn-services/vpn-service/vpn-id
| | +--:(l1vpn)
| | +--rw l1vpn-ref? -> /l1:l1cs/service/service-list/subscriber-l1vc-id
| +--rw (te)?
| +--:(actn-vn)
| | +--rw actn-vn-ref? -> /vn:actn/vn/vn-list/vn-id
| +--:(te-topo)
| | +--rw vn-topology-id? te-types:te-topology-id
| | +--rw abstract-node? -> /nw:networks/network/node/node-id
| +--:(te-tunnel)
| +--rw te-tunnel-list* te:tunnel-ref
+--rw site-mapping
+--rw mapping-list* [map-id]
+--rw map-id uint32
+--rw (service)?
| +--:(l3vpn)
| | +--rw l3vpn-ref? -> /l3:l3vpn-svc/sites/site/site-id
| +--:(l2vpn)
| | +--rw l2vpn-ref? -> /l2:l2vpn-svc/sites/site/site-id
| +--:(l1vpn)
| +--rw l1vpn-ref? -> /l1:l1cs/access/uni-list/UNI-ID
+--rw (te)?
+--:(actn-vn)
| +--rw actn-vn-ref? -> /vn:actn/ap/access-point-list/access-point-id
+--:(te)
+--rw ltp? te-types:te-tp-id

## Slide 7: Next Step
The authors believe that this draft is a good base for WG adoption.