## Slide 1: PCEP Extensions for Establishing Relationships Between Sets of LSPs and Virtual Networks (VN)
draft-leedhody-pce-vn-association-05
Young Lee | Dhruv Dhody | Xian Zhang | Daniele Ceccarelli

## Slide 2: ACTN VN Association
Last presented in IETF 98 (-02 version)
Associating a set of LSPs with a VN "construct" to facilitate VN operations via PCEP
Using ASSOCIATION object [I-D.ietf-pce-association-group]
  Associates a set of LSPs created/used for a particular VN.
  A new Association Type – VN Association Type
  Two TLVs
    VIRTUAL-NETWORK-TLV
    VENDOR-INFORMATION-TLV

## Slide 3: VN Association – Changes since -02
Alignment with ACTN framework changes
Alignment with Association group changes
Capability advertisement
Dynamic Association procedures
Others
Detail specification for the VIRTUAL-NETWORK-TLV
IANA Considerations

## Slide 4: VN Association – Why?
This ‘association’ allows the child/parent PCEs to identify which LSPs belong to a certain VN.
Does child PCE (acting as PNC) needs to be aware of this association?
  Child PCE are responsible for per-domain LSPs; Child PCE of ingress domain may also be responsible for E2E LSPs.
  Child PCE is made aware of the association between the partial set of LSPs under its preview.
  Parent PCE is aware of association between full set of LSPs under the VN.
The child/parent PCE could then use this association to optimize these LSPs (belonging to a VN) together and taking into consideration the impact on the other LSPs
The child/parent PCE could further take VN specific actions on the LSPs such as relaxation of constraints, policy actions, setting default behavior, as per the local policy identified for a VN.
  As compared to doing this per LSP

## Slide 5: VN Association
Parent Stateful PCE (MDSC)
Child Stateful PCE (PNC)
The VN Association help to find the per-domain LSPs (or E2E) that belong to the same VN.
During re-optimization, this relationship is factored in during path computation
Local Policy can be set per VN (rather than individually for each LSP)
Red VN
Blue VN

## Slide 6: Next Step
The document is stable and aligned to other documents in PCE/TEAS WG.
The association object is the right approach in PCEP.
Ready for WG Adoption poll!