## Slide 1: Traffic Engineering and Service Mapping Yang Model draft-lee-teas-te-service-mapping-yang-09
Young Lee, Huawei
Dhruv Dhody, Huawei
Daniele Ceccarelli, Ericsson
Jeff Tantsura, Nuage Networks
Giuseppe Fioccola, Telecom Italia
Qin Wu, Huawei
TEAS WG @ IETF 102

## Slide 2: TE-Service Mapping Model Update (1)
The role of TE-service Mapping model is to create a mapping relationship between -
  Services – L3SM, L2SM, L1CSM, etc.
  TE topo, TE tunnel model and the ACTN VN Model
  Update: Generalized it by making the model to have direct mapping to TE-topo and TE-tunnel as well!
This TE-service mapping model is needed to bind L3VPN, L2VPN, L1CSM specific service model with underlying TE-specific parameters.
This binding will facilitate a seamless service operation with underlay-TE network visibility and control.
L3SM
L2SM
TE-Service Mapping Model
ACTN VN
TE-topology
L1CSM
TE-tunnel
Generalization

## Slide 3: Issues discussed since IETF 101
An independent yang model for TE & Service Mapping v/s an augmentation of service yang model
  Single mapping model to map any service to various levels in TE (VN/Topo/Tunnel)
  Multiple models for each type of service – augmentation of L1/2/3 SM models.
This was discussed on the mailing list, discussions in favor of one TE & Service Mapping model that applied to all L1/2/3 SM models.
Mapping
ACTN VN
TE Topology
L3SM
L2SM
L1CSM
TE Tunnel
TE
Service
L3SM
TE Mapping
ACTN VN
L2SM
TE Mapping
L1CSM
TE Mapping
TE Tunnel
TE Topology
ACTN VN
TE Topology
TE Tunnel
ACTN VN
TE Topology
TE Tunnel

## Slide 4: TE-Service Mapping Model Update (2)
Reorganized Map Type (for VN/Tunnel selection policy)
New VN/Tunnel Binding
Customer could request a VPN service with a new VN/Tunnel not shared with other existing services.
VN/Tunnel Sharing
Customer could request a VPN where the tunnels can be shared with other existing VPNs.
VN/Tunnel Modify
This mode allows the modification of the properties of the existing VN/tunnel (e.g., bandwidth) when VN/Tunnel Selection Mode is applied.
Hard Isolation with deterministic characteristics
Hard Isolation
Soft Isolation

## Slide 5: TE-Service Mapping Model Update (3)
Introduced “Availability” for customer to indicate the level of availability.
  99.9999 %
  99.999 %
  99.99 %
  99.9 %
  99 %
This needs to be translated into network level policies - protection/reroute policies associated with VN/Tunnels.

## Slide 6: Yang Model
module: ietf-te-service-mapping
+--rw te-service-mapping
+--rw service-mapping
| +--rw mapping-list* [map-id]
| +--rw map-id uint32
| +--rw map-type? map-type
| +--rw (service)?
| | +--:(l3vpn)
| | | +--rw l3vpn-ref? -> /l3:l3vpn-svc/vpn-services/vpn-service/vpn-id
| | +--:(l2vpn)
| | | +--rw l2vpn-ref? -> /l2:l2vpn-svc/vpn-services/vpn-service/vpn-id
| | +--:(l1vpn)
| | +--rw l1vpn-ref? -> /l1:l1cs/service/service-list/subscriber-l1vc-id
| +--rw (te)?
| +--:(actn-vn)
| | +--rw actn-vn-ref? -> /vn:actn/vn/vn-list/vn-id
| +--:(te-topo)
| | +--rw vn-topology-id? te-types:te-topology-id
| | +--rw abstract-node? -> /nw:networks/network/node/node-id
| +--:(te-tunnel)
| +--rw te-tunnel-list* te:tunnel-ref
+--rw site-mapping
+--rw mapping-list* [map-id]
+--rw map-id uint32
+--rw (service)?
| +--:(l3vpn)
| | +--rw l3vpn-ref? -> /l3:l3vpn-svc/sites/site/site-id
| +--:(l2vpn)
| | +--rw l2vpn-ref? -> /l2:l2vpn-svc/sites/site/site-id
| +--:(l1vpn)
| +--rw l1vpn-ref? -> /l1:l1cs/access/uni-list/UNI-ID
+--rw (te)?
+--:(actn-vn)
| +--rw actn-vn-ref? -> /vn:actn/ap/access-point-list/access-point-id
+--:(te)
+--rw ltp? te-types:te-tp-id

## Slide 7: Next Step
This is quite a useful feature
The authors believe that this draft is a good base for WG adoption.